## Slide 1: TSM&O Solutions to Mitigate Wrong-Way Driving (WWD) Crashes on Arterials
2019 NOCoE TRANSPORTATION TECHNOLOGY TOURNAMENT
ITS - PCB

## Slide 2: Presentation Overview
Background
Study Corridors
Proposed Solutions
ITS Architecture
Deployment Costs and Timeline
Expected Benefits

## Slide 3: WWD Crashes
Wrong-way Driving (WWD) is the movement of vehicle in direction opposite to the one designated for travel
Type
Severity
Frequency
Proportion
Head-on and opposite
direction sideswipes
Incapacitating
injuries and
fatalities
350 fatalities
annually nationwide
3% crashes
on high
speed divided
highways
Attributes of
WWD crashes

## Slide 4: WWD Crashes on Arterials
Arterials are 2.3 times more likely to experience WWD incidents than freeways
Mitigating WWD incidents on arterials is more complicated as they have several access points
Frequency
Location
Streets
Time
1,890 crashes on arterials
(2012-2016)
> 50% of crashes intersection-related
13.5% crashes on one-way streets
> 64% of all fatal crashes at night
Florida Statistics

## Slide 5: Objectives
To assess the existing conditions on arterials that experienced frequent WWD crashes and incidents
To propose TSM&O solutions to mitigate WWD incidents on arterials
1
2
TSM&O Solutions
Traditional Solutions

## Slide 6: Study Corridors
N 22nd St & N 21st St
N Tampa St
2.7-mile section, one-way three-lanes
23 Stop Signs and 14 signals
8 WWD crashes 2012-2015
6 WWD arrests 2015-2019
1-mile, one-way pair of parallel segments
7 Stop signs and 7 signals
5 WWD crashes 2012-2015
13 WWD arrests 2015-2019

## Slide 7
Existing Conditions
What the Right-Way Drivers see
What the Wrong-Way Drivers see
6
1
Small and scattered
signs
3
No WW signs along the corridor
2
Obstructed
WWD Signs
Poor
lighting
5
WW signs
Not easily seen
4
Inconsistent
WW signage
Problems?

## Slide 8
Critical Locations with WWD Crashes
N
Vehicle 1 going eastbound on a westbound corridor
N
Vehicle 1 turning right to the wrong direction

## Slide 9: Proposed Solutions
Adding Directional Pavement Markings to Avoid Wrong Way Left Turns
Enhancement to Existing Signs
Innovative TSM&O
Solution
Enhancement to Traditional Signs
Quick Fixes

## Slide 10
IIRPMs
N Tampa St.
E Kennedy Blvd.
E Jackson St.
E Madison St.
Thermal Imaging Detection Cameras sending message to the Signal Controller
LED-lit “NO LEFT/RIGHT TURN & ONE WAY Signs
Detection-triggered “WRONG WAY” signs with LED Lights
Detected WW Driver
Flashing Red Signal activated after Detecting a WWD
Notification
Notification

## Slide 11: High-Level Functional Architecture

## Slide 12: Deployment
Cost Breakdown
Installed Technologies
No Turn LED Signs
Red IIRPMs
Thermal Imaging WW Detection System
Detection-triggered Wrong Way Signs with LED Lights

## Slide 13: Project Timeline
Stakeholder Consultation & Needs Assessment
Review of the ConOps
Procurement
System Deployment
System Testing & Validation
Year 2020
  Jan-Feb
  Feb-Mar
  Apr-May
  June-Oct
  Nov-Dec
Start-August 2019!

## Slide 14: Anticipated Benefits
Provide real-time alerts to road users
Reduce frequency of WWD incidents
Adapt to other situations e.g., EMS
Improve incident response time
Reduce traffic violations

## Slide 15: Thank You!
Team Members: Cecilia Kadeha
Henrick Haule
Md Sultan Ali
Hector Vargas
Faculty Advisor: Priyanka Alluri
Industry Advisor: Peter Hsu, FDOT District 7
Raj Ponnaluri, FDOT Central Office